## Slide 1: Introduction to Raspberry Pi and Linux workshop
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/intro-to-rpi
At SUTD
14 March 2015

## Slide 2: Components check
Raspberry Pi Model B
Micro-SD card
Micro-USB cable ( with power adapter)
Small Breadboard
LED
Push button
220-ohm Resistor
4 male-female jumper wires
LAN cable

## Slide 3: Download SSH client
Windows: Download Putty
Linux/Mac: Includes SSH client by default

## Slide 4: About me
Year 4 NUS Computer Science student
My Hardware projects with Arduino and Raspberry Pi

## Slide 5: What is a Raspberry Pi (RPi)?
“The Raspberry Pi is a low cost, credit-card sized computer that plugs into a computer monitor or TV, and uses a standard keyboard and mouse. It is a capable little device that enables people of all ages to explore computing, and to learn how to program in languages like Scratch and Python. It’s capable of doing everything you’d expect a desktop computer to do, from browsing the internet and playing high-definition video, to making spreadsheets, word-processing, and playing games.” http://www.raspberrypi.org/help/what-is-a-raspberry-pi/

## Slide 6: Common Rpi types today
Model A+
Model B+
2 Model B
700Mhz single-core ARMv6
256MB Ram
1 USB port
No Ethernet port
700Mhz single-core ARMv6
512MB RAM
4 USB ports
Ethernet port
900Mhz quad-core ARMv7
1024MB Ram
4 USB ports
Ethernet port
Power use:
Source: http://raspi.tv/2015/raspberry-pi2-power-and-performance-measurement

## Slide 7: Arduino vs Raspberry Pi
Specs | Arduino Uno | Raspberry Pi Model B+
CPU type | Microcontroller | Microprocessor
Operating System | None | Linux (usually Raspbian)
Speed | 16 Mhz | 700 Mhz
RAM | 2KB | 512MB
GPU/Display | None | VideoCore IV GPU
Disk | 32KB | Depends on SD card
GPIO pins | 14 digital pins (includes 6 analog) | 26 digital pins
Other connectivity | None | USB, Ethernet, HDMI, audio
Power consumption | 0.25W | 3.5W

## Slide 8: What is an Operating System (OS)?
An operating system (OS) is software that manages computer hardware and software resources and provides common services for computer programs.
  Source: http://en.wikipedia.org/wiki/Operating_system
My definition:
  A giant piece of software that gives programs you download/write hardware features in a standardised manner.
Closed-source vs open-source
  Closed: Windows, Mac OS X
  Open: Linux, FreeBSD, FreeDOS
Unix(-like) vs non-Unix
  Unix: Linux, Mac OS X
  Non-Unix: Windows

## Slide 9: Powering up your Raspberry Pi
Connect the following first
  SD card
  HDMI cable
  Keyboard/mouse
Connect this last
  Micro-USB cable

## Slide 10: First boot/Setup with raspi-config

## Slide 11: Enlarge root partition

## Slide 12: Boot desktop options

## Slide 13: Select graphical option

## Slide 14: Internationalisation options

## Slide 15: Change timezone

## Slide 16: Select Asia/Singapore timezone

## Slide 17: Change keyboard layout

## Slide 18: Change to English (US) layout
We don’t want the default UK layout
-> Generic 105-key (intl) PC
-> Other
-> English (US)
-> English (US)
-> The default keyboard layout
-> No compose key
-> “Yes” to terminate X server

## Slide 19: Enable camera (optional)

## Slide 20: Advanced Options

## Slide 21: Enable SSH (remote access)

## Slide 22: Reboot when complete

## Slide 23: Initial setup complete!

## Slide 24: SSH connection and terminal
Use “ifconfig” to get IP address
  ifconfig
  Look under “eth0”
Windows
  Putty: Hostname: x.x.x.x, Port: 22
Mac/Linux
  Open terminal
  ssh pi@x.x.x.x

## Slide 25: Raspbian default username/password
Username: pi
Password: raspberry

## Slide 26: Unix basics
Show directory contents:
  (Do this after every command below to see what has changed)
  ls or ls -l
Make directory:
  mkdir lesson
Change directory:
  cd lesson
Create an empty file:
  touch myfile
Edit file with nano:
  nano myfile
  Type something random inside the text editor then press Ctrl+X to save and quit.
View file quickly:
  cat myfile
Copy file
  cp myfile myfile2
Remove file:
  rm myfile
Move file
  mv myfile2 myfile

## Slide 27: Other useful commands
Command | Purpose
man | Get information about a particular command. Eg: man ls
ifconfig | Get network information like IP address
adduser | Create user
passwd | Change password
uname –a, uname -r | Show OS information
history | Shows past commands you ran
chmod | Change permissions of a file/directory

## Slide 28: Multi-user environment: Root vs non-root vs sudo
root (privileges)
  One administrative user that can do anything
  Most Linux distributions have root by default except for Ubuntu, Raspbian
  Required for hardware access, package installation etc
non-root
  Only restricted to activities in home (~) directory
sudo
  Command to let certain non-root users temporarily get root privileges
  Prepend in front of command that needs root
    Eg: sudo apt-get install java

## Slide 29: Package management
Install software from online repositories
Maintains dependencies for you
All these software come as packages
  Firefox, nano, sudo

## Slide 30: Using a package manager -installing htop
Always run before package installation
  Update local repository index
    sudo apt-get update
  Upgrade all out-of-date packages
    sudo apt-get upgrade
Install htop
  sudo apt-get install htop
Htop:
  Process information viewer like Windows Task Manager
*Skip this slide if no internet connection

## Slide 31: Header pins
26 Digital-only General Purpose Input Output pins
Includes i2C and SPI
3.3V logic levels
No analog-digital-converter
  Use external ADC like MCP3008

## Slide 32: Using the GPIO pins
Python programming language
LED
Button

## Slide 33: Before handling GPIO
Always shut down the Rpi
sudo poweroff
Side note: Unlike the Arduino, Rpi needs to be shutdown properly before pulling the power.

## Slide 34: LED and Button Connection

## Slide 35: LED code
1. Open command line text editor: nano gpio.py
2. Type the code on the left
3. Quit nano with Ctrl+X
4. Run code: sudo python gpio.py
Result:
LED should blink at 1 second intervals
Watch your indentation. Python is indentation-sensitive

## Slide 36: LED and button code 1
1. Quit the previous program using Ctrl+C
2. Modify your previous code:
nano gpio.py
3. Run again:
sudo python gpio.py
Now try pressing the button a few times.
What do you notice? Why?

## Slide 37: LED and button code 2 (Debouncing)
Does it work properly now?

## Slide 38: Now lets use the process viewer
Keep the previous code running
Open another terminal or SSH connection
Run the process viewer
  htop
  If you did not install htop: “ps aux | grep python”
What do you notice about Python’s CPU usage? Why?

## Slide 39: LED and button code 3 (Avoid high CPU consumption)
What is Python’s CPU usage now?

## Slide 40: Camera hardware connection
1. Lift up the top connector

## Slide 41: Camera hardware connection
2. Insert the Flexible Flat Cable (FFC), note the position of the blue strip.

## Slide 42: Camera hardware connection
3. Lock the connector back

## Slide 43: Python camera code

## Slide 44: Some useful addons
Cobbler
Case
USB-TTL cable

## Slide 45: 3.3V USB-TTL cable
An alternative way of interacting with your Rpi without keyboard and HDMI screen
https://www.adafruit.com/product/954
Windows
  Check COM number n from Device Manager
  Putty, Serial COMn, Speed 115200
Mac/Linux
  Install screen
  Linux: screen /dev/ttyUSB0 115200
  Mac: screen /dev/tty.usbserial 115200

## Slide 46: Sharing SD cards between Rpi 2 and others
May not always be swappable
Some distributions like Arch Linux have ARMv7 specific packages
No issue with Raspbian as of now

## Slide 47: Further reading
GPIO interrupts
Other RPi operating systems like Arch Linux ARM
Read-only file system if you need unsafe poweroff
Mini-UPS for unsafe power off

## Slide 48: Q&A